## Slide 1: Publishing and Consuming Government Linked Data on the Semantic Web
Ghislain Auguste Atemezing
Multimedia Department, Eurecom
Supervisor:
Dr. Raphaël Troncy, MM Department, Eurecom

## Slide 2: Outline
Introduction
Research Questions
Contributions
  Semantic publishing of geospatial data
  Visualizations of Government Linked Data
  Best Practices for metadata in vocabularies
Conclusion
Publications

## Slide 3: Research Questions
How to efficiently represent and store geospatial data on the Web to ensure interoperable applications?
  the publication of real datasets
  the interlinking with other datasets having overlapping coverage
What are the best options for a user to discover, browse and interact with semantic content?
  Can we propose a generic model for visualizing semantic content?
What are the mechanisms to help preserving structured data of a high quality on the Web?
  How to improve reusing vocabularies for better interoperability
  How to detect incompatibility between data and metadata
Notes: The answers to these Use Cases need to do some screen scraping on different html pages of data portals where the applications are described, sometimes without many information nor description.

## Slide 4: Part 1
Modeling, Interconnecting and
Generating Geodata on the Web

## Slide 5: Geospatial data: why it matters?
“80% of needs for decisions from public authorities have a geospatial component”.
(Philippe Grelot, IGN-France)

## Slide 6: Scenario: 7th Arrondissement of Paris

## Slide 7: GeoData on the LOD Cloud
Linking Open Data cloud diagram 2014, by Max Schmachtenberg, Christian Bizer, Anja Jentzsch and Richard Cyganiak.
http://lod-cloud.net/
http://lod-cloud.net/versions/2014-08-30/

## Slide 8: French IGN- Reference Geodata
Different databases with overlapping information: BD ORTHO, BD PARCELLAIRE, POINT ADRESSE, BD ALTI 25m, BD TOPO; etc.
CRS: LAMBERT93 or RGF93
Q: ”Give me all the bridges in a radius of 2km from the "Eiffel Tower“?
A: Not straightforward
« ..describes the French national territory and the occupation of its land, elaborates and updates perpetual inventory of the forest resources »
Notes: Files available in SHP, pdf
Information overlap in different products, sometimes referring to the same « real world » concepts.

## Slide 9: Coordinate Reference Systems (CRS)
A representation of the locations of geographic features within a common geographic framework
Each CRS is defined by its measurement framework
  Geographic: spherical coordinates (unit: decimal degrees)
  Planimetric: 2D planar surface (unit: meters) + a map projection
  Additional measurement properties: ellipsoid, datum, standard parallels, central meridians, etc.
Situation:
  Several hundred Geographical Coordinate Systems (WGS84, ETRS89, etc.)
  Several thousands Projected Coordinate Systems (UTM, Lambert93, etc.), http://resources.esri.com/help/9.3/arcgisserver/apis/rest/pcs.html

## Slide 10: Current Tooling and Limitations
Circé: A Converter Software from IGN
  Allows conversion between some France CRSs to WGS84
  Closed Source, No open service
Existing Web tools (e.g., world coordinate converter)
  No open service, closed source
  Converting algorithms don’t usually map to any national mapping authority.
Contribution: a web based service to perform conversion between various CRSs.
  The integration of such a converter can ease the process of the publishing different types of geometries on the web regardless of their Coordinates systems.

## Slide 11: Developing a REST converter service
International Communication
Many regional's’ published data involve with local CRS
A medium
Interpret the coordinates between these CRSs
A Converter Service
Open services for community
RESTFul Web Service

## Slide 12: Implementation - Evaluation
WGS 84 <–> Lambert 93 Algorithms
Conversion from WGS 84 to Lambert 93 |  |  |  |  |  | 
Tools | Input |  |  | Output |  | 
 | Latitude (DD) | Longitude (DD) |  | X (m) |  | Y (m)
Geo Converter | 43.700594 | 7.277959 |  | 1044752.61 |  | 6298403.61
Circé |  |  |  | 1044752.20 |  | 6298404.17
twcc.free.fr |  |  |  | 1044752.61 |  | 6298403.61
Conversion from Lambert 93 to WGS 84 |  |  |  |  |  | 
Tools | Input |  | Output |  |  | 
 | X (m) | Y (m) | Latitude (DD) |  | Longitude (DD) | 
Geo Converter | 1044752.61 | 6298403.61 | 43.700594 |  | 7.277959 | 
Circé |  |  | 43.700589 |  | 7.277964 | 
twcc.free.fr |  |  | 43.700594 |  | 7.277959 | 

## Slide 13: Implementation - Evaluation
WGS 84 <–> UTM Algorithms

## Slide 14: Vocabularies for Modeling Features (1/2)
Authority list of terms (e.g. Foursquare)
  Less structured
  Represent categories of Points of Interest (POIs)
  Typically, one type as an API answer
  Need to express the semantics of the terms
SKOS Categories (e.g. GeoNames)
  Classes are skos:conceptScheme
  Codes are skos:Concept
  Few classes … BUT many codes

## Slide 15: Vocabularies for Modeling Features (2/2)
Domain specific ontologies
  One ontology per subdomain (transport, administrative unit, hydrography, etc.)
  Interconnected ontologies (by explicit semantic e.g. owl:imports)
  UK (OS) – ES (GeoLinkedData)
Some richer ontologies created by (semi-)automatic tools / NLP
  Deeper taxonomy to structure the ontology
  LinkedGeoData: 16 high-level classes, 1294 classes
  GeOnto: 2 high-level classes, 783 classes in total

## Slide 16: Modeling Geometry
Point (lat/long)
  WGS 84 vocabulary described by W3C
Rectangle (“bounding box”)
  Geopolitical Vocabulary (FAO)
Points in a List
  Sequence of points (LinkedGeoData)
  An object is “formedBy” a ListOfPoints (GeoLinkedData.es)
Literals (GML datatype in RDF)
  Ordnance Survey (UK)
More structured representation of complex geometry
  NeoGeo Vocabulary (GeoVocamp), http://geovocab.org/
Notes: Five approaches for modeling the Geometry: Point, Rectagne, Points in a List, Points in a group of RDF resources, Literals and more structured

## Slide 17: Reusing Existing Ontologies (GeOnto)
Ontology for geographic objects (POI)
  Output of a French (ANR) research project
  Obtained from NLP tools
Classes in French
  rdfs:labels in FR & EN
  No rdfs:comments
  Few owl:ObjectProperty
  783 classes
Overlap with other vocabs
  Need for alignment

## Slide 18: Aligning GeOnto with existing Ontologies
Alignment of GeOnto with 4 ontologies and 2 more simple taxonomies
  LGD, DBpedia, Schema.org, GeoNames
  Foursquare, Google Places
Goal: finding owl:equivalentClass
  Tool : Silk framework
  Metrics : LevenshteinDistance, Jaro
  Labels : @en des classes
  Aggregation Function: Mean
Manual validation
  For « rdfs:subClassOf »
  Specific alignments with GeoNames codes

## Slide 19: Alignment Process (GeoNames)– Results
Silk
Look for skos codes that matches GeOnto classes
Verify the links <70%
SPARL Endpoint
Use SPARQL « Construct » to generate a new graph.
Alignment File
Export the rdf file
Generate « sameAs » links
Vocab/taxonomies | #Classes | #Classes aligned
LGD | owl:Class: 1294 | 178
DBpedia | owl:Class: 366 | 42
Schema.org | owl:Class: 296 | 52
GeoNames | skos:Concept: 699 | 287
Foursquare | 359 | 46
Google Place | 126 | 41
bdtopo | owl:Class: 237 | 153
High precisions > 80%,
BUT P(Schema.org) = 50%. GeOnto entities are more specific to France

## Slide 20: CheckList for vocabulary modeling
Complex Geometry Coverage
  Need to publish more data with complex geometries
  Reuse and extend suitable ontologies
  NeoGeo
  GeoSPARQL
Features MUST be connected to Geometry
  Sometimes it may requires two namespaces
Serialization
  Provide serialization in other GIS formats (GML, WKT, KML, etc.)
Literal vs Structured Representation
  Use of structured representation for complex geometry
  This covers some of the Use Cases at IGN
To be extended with:
Structured geometries
Keep compatibility with GeoSparql (wktLiteral)
A property for associating anything to a geometry
A property for associating geometries to one given CRS
Notes: GeoSPARQL needs to be published with (de)-referenceable URIs?! We want to have GeoSPARQL in the LOV catalog.

## Slide 21: Vocabulary for Geometry
Extending and reusing existing vocabularies
  Available at http://data.ignf.fr/def/geometrie
@prefix ngeo: <http://geovocab.org/geometry#>.
@prefix sf: <http://www.opengis.net/ont/sf#>.
[…]
geom:Geometry a owl:Class;
rdfs:comment "Primitive géométrique non instanciable, racine de l'ontologie des primitives géométriques. Une géométrie est associée à un système de coordonnées et un seul."@fr;
rdfs:label "Géométrie"@fr, "Geometry"@en;
owl:equivalentClass [ a owl:Restriction;
owl:onClass ignf:CoordinatesSystem;
owl:onProperty geom:crs;
owl:qualifiedCardinality "1"^^xsd:nonNegativeInteger];
rdfs:subClassOf ngeo:Geometry;
rdfs:subClassOf sf:Geometry.
Notes: GeoSPARQL needs to be published with (de)-referenceable URIs?! We want to have GeoSPARQL in the LOV catalog.

## Slide 22: Associating CRS to Geometries
A vocabulary for describing CRS
  Subset of ISO 19111 model
  Available at http://data.ignf.fr/def/ingf
A dataset for French CRS
  Convert from XML data published by IGN France to RDF
  Eg: “Lambert 2 étendu” http://data.ign.fr/id/ignf/crs/NTFLAMB2E
Notes: GeoSPARQL needs to be published with (de)-referenceable URIs?! We want to have GeoSPARQL in the LOV catalog.

## Slide 23: Overview of the Geo-vocabularies
Notes: GeoSPARQL needs to be published with (de)-referenceable URIs?! We want to have GeoSPARQL in the LOV catalog.

## Slide 24: Datalift: A tool for publishing LinkedData
A SET of modular tools for “lifting raw data in rdf.
Notes: GeoSPARQL needs to be published with (de)-referenceable URIs?! We want to have GeoSPARQL in the LOV catalog.

## Slide 25: GEOFLA®: French Administrative Dataset
GEOFLA® Dataset on French administrative units
Geofla metadata on CRS
http://professionnels.ign.fr/sites/default/files/DC_GEOFLA_1-1.pdf
Open Licence

## Slide 26: French Reference Geodata Mappings
Mapping results with external dataset |  |  | 
GEOFLA DATASET |  | #mappings | Tool
 | INSEE | 37,020 | SILK
 | DBPEDIA-FR | 23, 252 (communes) and 93 departments | LIMES
 | NUTS | 105 (16 regions) | SILK
 | GADM | 70 | SILK
GAZETTEER | LINKED GEODATA | 654 (lgdo:Amenity) | LIMES
Geofla dataset: Features are of type http://data.ign.fr/geofla
French Gazetteer: Features are of type http://data.ign.fr/topo
(GeOnto++)

## Slide 27: French Open Addresses in RDF Mappings

## Slide 28: Contribution to the LOD Cloud (FrLOD)
340 millions of triples in RDF (10% of DBPedia 2014)

## Slide 29: Part Two
Generating Visualizations
For Linked Data

## Slide 30: Why visualizations matter?
Many structured datasets are now available on the Web (e.g., 3 billions of Triples for Dbpedia 2014 release)
RDF is not what we show to end-users
InfoVis community has mature tools and studies on visualizing information.
Triples are good, but need to be “beautiful” for end-users.
In the era of “structured big data”, we also need tools for Web – based visual analysis and reporting.
Notes: The answers to these Use Cases need to do some screen scraping on different html pages of data portals where the applications are described, sometimes without many information nor description.

## Slide 31: Goal and Scenarios
Goal: Describe common patterns of visualization applications from Government Data Portals to make them reusable and interoperable
Use case 1: “Give me applications in Government Linked Data platforms in the domain of taxes”
Use case 2: “Find me apps running on Android in data.uk.gov for finding the nearest drugstores”
Use case 3: “How many free or inexpensive applications are available using US datasets in Health and Insurance domains”

## Slide 32: Types of Visualization in Government Portals
Study of applications consuming Open Data
  Countries: UK (7), USA (3) and France (3)
  Number of applications: (13)
  Domain: education, health, transport, government, city, housing, criminality, foreign aid
Classification dimensions
  Platform (web, mobile), data sources, which views are available (maps, charts, timeline, etc.)
  URL policy for identifying data objects
  License for the application / for the data
  Commercial / non-commercial

## Slide 33: Linked Data Application Categories (*)
Generic applications
  Used to browse any RDF graph (e.g: Tabulator, OpenLink Data Explorer)
Vocabulary-specific applications
  Built around particular vocabularies (e.g.: FaceBook Social Graph API, IsaViz, CubeViz)
Data-specific applications (mashups)
  Built around particular datasets (e.g. Where does my money go, IOGDS: International Open Government Dataset Search)
(*) Classification according to:Jeni Tennison : http://www.jenitennison.com/blog/node/126

## Slide 34: Relevant Features in Visualization Tools
Data format given as input (csv, xml, shp, rdf, etc.)
Data access (API, dump, etc.)
Language code
Type of view
External Libraries
License
Metadata: author, organization
Notes: Importance of each feature:
* Data formats: the type of the format could lead to the decision of creation a converter layer before the visualization layer.
Data access: defines how to get the data, such as simple dump, API, SPARQL endpoint
Language code: this helps deciding also for the integration of tool.
Type of view is essential depending on the type of the data to display. E.g: if the tool does not provide timeline view, it could be difficult to want to create a visualization making use of timeline.
* External libraries are useful for integration compatibility.
* License for reusability of the tool
* Author/creator for metadata mention of the owner or the tool

## Slide 35: Describing an Application: Opendatacom
Scope/Domain: Department for Communities and Local Government, datasets access
Description: visualize available datasets (finance, housing, deprivation, geography) by authorities or postcode.
On the dashboard, it provides graphs showing the national distribution of a district and how the values for this local authority compare with others in England.
Supported Platform: Web
URL Policy: http://{domain}/id/{...} with redirection to the corresponding document at: http://{domain}/doc/{...}.
Hampshire County Council is: http://opendatacommunities.org/id/county-council/hampshire
Data Sources: 36 datasets from DCLG, Administrative Geography and Postcodes from Ordnance Survey.
Type of View: Graph, Map views.
Visualization Tools: google visualization API, raphael.js
License: Open Government license [OGL]
Business Value: Non commercial

## Slide 36: DVIA: A vocabulary to describe Applications
dvia: Application
dct:title
dvia:description
dvia:keyword
dvia:url
dct:creator
dvia:businessValue
dvia:scope
dvia:view
dctype:Software
dvia: Platform
dct:title
dvia:system
dvia:preferredNavigator
dvia:alternativeNavigator
dvia: VisualTool
dct:title
dct:description
dvia:accessUrl
dvia: downloadUrl
dcat: Dataset
dct: title
dcat: accessURL
dct:references
dcat: keyword
org:Organization
dvia:designBy
dvia:consumes
dvia:usesTool
dvia:platform
Prefixes:
@prefix dct: <http://purl.org/dc/terms/>.
@prefix dcat: <http://www.w3.org/ns/dcat#>.
@prefix dctype: <http://purl.org/dc/dcmitype/>.
@prefix org: <http://www.w3.org/ns/org#>.
@prefix dvia: <http://data.eurecom.fr/ontology/dvia#>.

## Slide 37: DVIA in Real World Datasets
Applications of DVIA
  Scrap and reconcile data from apps contests: see the upcoming catalog from Apps4Europe
  Use to populate 22 past events of hack-athons in Europe, with 889 applications
  Implementation of a universal JavaScript plugin to embed RDFa in organizers events.
  An extension for Wordpress uses DVIA
Notes: *The Apps4Europe project, recently release a big catalog of all Apps in Europe and the goal now is to make some script for populating DVIA.
  * Towards Linked Open Visualizations (LOVIZ) catalog

## Slide 38: Challenges for Generic Visualizations
“Don’t ask what you can do for
the Semantic Web; ask what
The Semantic Web can do for you!” (D. Karger, MIT CSAIL) –
1- How to build bridge to fill the gap between traditional
InfoVis tools and Semantic Web technologies
2- How can Semantic Web help in visualization?

## Slide 39: A Journey of a Web Application developer
Scenario 1:
  Known Datasets, Known vocabularies  Specific SPARQL queries
  Visualizations: dataset specific
Example
  Datasets on schools in France
  Vocabularies: geo vocab, data cube, geometrie,
  Application: PerfectSchool

## Slide 40: A Journey of a Web Application developer
Scenario 2:
  Unknown Datasets, Known domains, so domain-specific SPARQL queries
  Visualizations: domain specific
Example
  Endpoints of geodatasets
  Domain: geospatial
  Application: GeoRDFviz

## Slide 41: A Journey of a Web Application developer
Scenario 3:
  Unknown Datasets, Unknown domains, so generic SPARQL queries
  Visualizations: adapted to domains specific
Example
  Any endpoints
  Multiple domains: geodata, statistics, persons, cross-domains, etc..
  Application: ?????
Related work on configuring Semantic Web widgets by data mapping. [1]
Application: Efficient search for Semantic News demonstrator
in Cultural Heritage Dataset
Tool: ClioPatria
[1] Hildebrand, Michiel, and Jacco Van Ossenbruggen. "Configuring semantic web interfaces by data mapping."
Visual Interfaces to the Social and the Semantic Web (VISSW 2009) 443 (2009): 96.
…but “method not apply to create
interfaces on top of arbitrary
SPARLQ endpoints”

## Slide 42: Our Proposal
Linked Data
Vizualization
Wizard (LDVizWiz)

## Slide 43: Requirements of LDVizWiz (LDViz-”Wise”)
Predefined categories associated to visual elements
Build on top of RDF standards
  e.g., SPARQL queries ; Semantic Web technologies
Reuse existing Visualization libraries
  e.g., Google Maps, Google Charts, D3.js, etc.
Input: Datasets published as LOD
Reuse Information Visualization Taxonomy
Target to non “RDF/SPARQL speakers”

## Slide 44: Mapping Categories and vocabularies
Geographic information
  geo: vocab, schema:Place, etc.
Temporal information
  Time, interval ontologies
Event information
  lode, event, sport, etc..
Agent/Person
  foaf:Person/foaf:Agent
Organization information
  ORG vocabulary, foaf:Organization
Statistics information
  Data cube, SDMX model
Knowledge information
  Schemas, classifications using SKOS vocabulary

## Slide 45: LDVizWiz Workflow

## Slide 46: Step 1: Categories detection
Detection of main categories in datasets
  ASK SPARQL queries on predefined categories
  Uses well-known vocabularies in LOV
  Unveil main facets of the visualizations
  Condition the type of visual elements
Detection

## Slide 47: Experiment: Categories Detection
Category | Number | %
GEO DATA | 97 | 21.84%
EVENT DATA | 16 | 3.60%
TIME DATA | 27 | 6.08%
SKOS DATA | 02 | 0.45%
ORG DATA | 48 | 10.81%
PERSON DATA | 59 | 13.28%
STAT DATA | 29 | 6.6%
444 endpoints (*) analyzed, 278 good answers (62.61%) using ASK queries.
Few taxonomies in SKOS, many GEO DATA
Applications
  Automatic detection of endpoints categories
  More “trustable” than human tagging
  Map categories detected with “suitable” visual elements for the visualizations (e.g., TimeLine +maps for events data)
(*) All the endpoints retrieved from sparqles.org

## Slide 48: Step2: Properties Aggregation
Goal: Exploit the “connectors” between graphs
“connectors” are used to enrich a given graph
  e.g., owl:sameAs ; rdfs:seeAlso, skos:exactMatch
Retrieve properties from external datasets
  So called “enriched properties”
Build candidate properties for visualization
  For pop-up menus
  For facet browsing
  For charts display
Detection
Aggregation

## Slide 49: Step3: Publication
Visualization Generator
  Recommend the visual elements based on categories
  Transform ASK queries to SELECT or CONSTRUCT queries for input to visual library.
Visualization Publisher
  Export the description of visualization in RDF
  Add metadata for the visualization (charts) and steps used to create it.
  e.g., dcat:Dataset, prov:wasDerivedFrom, void:ExampleResource, chart vocabulary
Detection
Aggregation
Publication

## Slide 50: Current Implementation
Javascript light version as “proof-of-concept”
Url: http://semantics.eurecom.fr/datalift/rdfViz/apps/

## Slide 51: Part Three
Best Practices for metadata in vocabularies

## Slide 52: Disambiguating Vocabulary Prefixes
Goal: align services against Linked Open Vocabularies to harmonize and manage vocabularies’ namespaces
LOV
PREFIX.CC
What <wo> namespace
stands for?

## Slide 53: Why if … global use of prefixes
Global namespaces
  With good practices to recommend a prefix
  Have a more transparent list of built-in prefixes
  All the services understand each other with prefixes
  Some de facto prefixes emerging: rdfs:, foaf:, rdf: owl:, skos:,

## Slide 54: LOV in a Nutshell : http://lov.okfn.org/dataset/lov/
A curated list of vocabularies
  More than 450 vocabularies
  Each of them described by vocabulary-of-a-friend (voaf)
  Provide a dump in N3 of the different versions of a vocabulary
  Quasi linearity of the growth, started with 75 vocabularies
The glitch in 2012 corresponds to the migration to OKFN hosting

## Slide 55: LOV vs PREFIX.CC-Alignment Findings
Chart: Findings during alignment process
| lov-able vocabs | Intersect-prefixes | vocabs in LOV | vocabs in prefix.cc
Number | 227 | 188 | 321 | 925
Category | Number
lov-able vocabs | 227
Intersect-prefixes | 188
vocabs in LOV | 321
vocabs in prefix.cc | 925
More than 200 prefixes in prefix.cc
are vocabularies


## Slide 56: Vocabulary Search and Ranking
Goal: Ranking vocabularies based on Information Content Metrics
Metrics
  Information Content Metric (IC): value of information associated with a given entity
  Partition Information Content Metric (PIC)
  Proposed a ranking based on IC and PIC

## Slide 57: Ranking Algorithm
1- Candidate terms selection in LOV
2- Grouping terms by namespace & weight assignment
3- Compute IC score
4- Compute PIC score
Output ranking

## Slide 58: Running Example: dcterms vs foaf
dcterms: http://purl.org/dc/terms/
Candidate terms: 53 (39 properties + 14 classes)
wf = 1+ 2+3 = 6
PIC = 1724.844
foaf: http://xmlns.com/foaf/0.1/
Candidate terms: 35 (26 properties + 9 classes)
wf = 1+ 2+ 3 = 6
PIC = 1033.197
PIC(dcterms) > PIC(foaf)

## Slide 59: Results on Ranking
Top-15 terms (IC value)
Top-15 vocabs (PIC value)

## Slide 60: Applications of the Ranking Metrics
Vocabulary life-cycle management
  Help assessing the use of terms and vocabulary updates
  Monitoring the use of http://www.w3.org/2003/06/sw-vocab-status/ns#:term_status or owl:deprecated
Semantic Web applications
  Vocabularies with higher PIC might be proposed to a user as much as possible, e.g. for choosing properties to display in a facetted browsing interface
Interlinking datasets
  Generate sameAs links between resources based on vocabularies terms with lower IC value

## Slide 61: Licenses Compatibility
Goal: Reasoning on Licenses for checking compatibilities between vocabularies and datasets
Approach:
  Licenses retrieval both for the dataset and for the vocabularies used in the dataset.
  Deontic logic to compute compatibility

## Slide 62: LIVE Framework
http://www.eurecom.fr/~atemezin/licenseChecker/
Notes: The answers to these Use Cases need to do some screen scraping on different html pages of data portals where the applications are described, sometimes without many information nor description.

## Slide 63: The Logic
RDF licenses: http://purl.org/NET/rdflicense
Logic of deontic rules:
  constructive account of basic deontic modalities (obligation, prohibition, permission)
  compute the set of all conclusions for each license and then check whether incompatible conclusions are obtained.

## Slide 64: Evaluation
LIVE provides the compatibility in less than 5 seconds for 7 datasets
LIVE retrieves 48 vocabularies in less than 14 seconds
Notes: *The Apps4Europe project, recently release a big catalog of all Apps in Europe and the goal now is to make some script for populating DVIA.
  * Towards Linked Open Visualizations (LOVIZ) catalog

## Slide 65: Conclusion
We have presented models for Geodata
  For better handling complex geometries
  Supporting *all* CRS
  For easy querying in SPARQL
We have proposed a generic visualization wizard
  Based on predefined categories
  Targeted to lay-users
We have contributed in managing vocabulary metadata
  Disambiguating prefixes between vocabularies
  Improving vocabulary search and ranking
  Providing a license compatibility framework
  Contributing to Best Practices standard
Notes: *The Apps4Europe project, recently release a big catalog of all Apps in Europe and the goal now is to make some script for populating DVIA.
  * Towards Linked Open Visualizations (LOVIZ) catalog

## Slide 66: Future Work
Managing Data updates and versioning
  Versioning: integrate Memento protocol?
  Spatio-temporal evolution
Multiple representation: need for metadata?
  Level of detail
  Geometry modeling rules and reasoning
Tracking Provenance of geodata
  To ensure quality of published dataset
  To ensure trust from application consumers
Notes: *The Apps4Europe project, recently release a big catalog of all Apps in Europe and the goal now is to make some script for populating DVIA.
  * Towards Linked Open Visualizations (LOVIZ) catalog

## Slide 67: Future Work
Visualizations
  Extend categories and vocabularies for detection
  Provide templates for generating “mash-ups” to combine domains, an mash-up widget generator
  Investigate the “importance” of a category in dataset
  Provide a user evaluation
Metadata management
  Publish a list of common recommended prefixes
  Foster and support current effort towards a more sustainable governance of vocabularies.
  Compare (P)IC with other graph-based ranking (e.g. pagerank)
  Investigate the dependency ranking between vocabularies
Notes: *The Apps4Europe project, recently release a big catalog of all Apps in Europe and the goal now is to make some script for populating DVIA.
  * Towards Linked Open Visualizations (LOVIZ) catalog

## Slide 68: Publications
Pierre-Yves Vandenbussche, G.A. Atemezing, Maria Poveda, Bernard Vatant: Linked Open Vocabularies (LOV): a gateway to reusable semantic vocabularies on the Web. Semantic Web Journal, under review, 2015.
G.A. Atemezing, Raphael Troncy: Modeling visualization tools and applications on the Web. Semantic Web Journal, under review, 2015.
G.A. Atemezing et al.: Transforming meteorological data into linked data. In Semantic Web journal, Special Issue on Linked Dataset descriptions, 2012. IOS Press.
Guido Governatori, Ho-Pun Lam, Antonino Rotolo, Serena Villata, G.A. Atemezing and Fabien Gandon: LIVE: a Tool for Checking Licenses Compatibility between Vocabularies and Data.(ISWC 2014, Demo Track)
G.A. Atemezing and Raphael Troncy: Information content based ranking metric for linked open vocabularies. (SEMANTICS 2014)
Ahmad Assaf, G.A. Atemezing, Raphael Troncy and Elena Cabrio: What are the important properties of an entity? Comparing users and knowledge graph point of view. In 11th Extended Semantic Web Conference (Demo Track, ESWC 2014)
Notes: *The Apps4Europe project, recently release a big catalog of all Apps in Europe and the goal now is to make some script for populating DVIA.
  * Towards Linked Open Visualizations (LOVIZ) catalog

## Slide 69: Publications
Bernadette Hyland, G.A. Atemezing and Boris Villazón-Terrazas (editors): Best Practices for Publishing Linked Data. W3C Working Group Note pub- lished on January 9, 2014. URL: http://www.w3.org/TR/ld-bp/
Bernadette Hyland, G.A Atemezing, Michael Pendleton, Biplav Srivastava (editors): Linked Data Glossary. W3C Working Group Note published on June 27, 2013. URL: www.w3.org/TR/ld-glossary/
Francois Scharffe, G.A Atemezing, Raphael Troncy, Fabien Gandon, Serena Villata, Bénédicte Bucher, Faycal Hamdi, Laurent Bihanic, Gabriel Kepeklian, Franck Cotton, Jerome Euzenat, Zhengjie Fan, Pierre-Yves Vandenbussche and Bernard Vatant: Enabling linked-data publication with the datalift platform. (AAAI, W10:Semantic Cities, 2012)
G.A. Atemezing and Raphael Troncy: Vers une meilleure interopérabilité des donneés geographiques francaises sur le Web de donneés. (IC 2012).
Houda Khrouf, G.A. Atemezing, Thomas Steiner, Giuseppe Rizzo and Raphael Troncy: Confomaton: A conference enhancer with social media from the cloud. (ESWC 2012, Demo Track)
Notes: *The Apps4Europe project, recently release a big catalog of all Apps in Europe and the goal now is to make some script for populating DVIA.
  * Towards Linked Open Visualizations (LOVIZ) catalog

## Slide 70: Thank you for your attention!